## Slide 1: The Western Design Center, Inc. (WDC), Supplier of 65xx IC’s, IP, and Development Tools

## Slide 2: 8–bit Microprocessor W65C02S
The W65C02S is a low power 8-bit microprocessor utilized in a vast array of products for the Automotive, Consumer, Industrial, and Medical markets.
Product Features:
Wide operating voltage range from 1.8V to 5V
Low Power consumption, 150uA@1MHz
16-bit address bus providing access to 65,536 bytes of memory space
Variable length instruction for code optimization

## Slide 3: 16–bit Microprocessor W65C816S
The W65C816S extends the 65xx technology family to handle 16-bit processing while maintaining low power features.
Product Features:
Emulation mode allows complete hardware and software compatibility with 6502 designs
24-bit address bus provides access to 16 MBytes of memory space
Separate program and data bank registers allow program segmentation or full linear addressing
New Direct Register and stack relative addressing provides capability for re-entrant, re-cursive and re-locatable programming

## Slide 4: 8–bit Microcontroller W65C134S
The W65C134S is a feature rich 8-bit microcontroller based on the W65C02S.
Product Features:
W65C02S CPU
Embedded Debug Monitor ROM
Debug port UART with baud rate timer
192 bytes of SRAM
56 I/O Lines
(2) 16-bit timers
Low power Serial Interface Bus (SIB) configured as a token passing Local Area Network
Monitor "Watch Dog" Timer with "restart" interrupt

## Slide 5: 16–bit Microcontroller W65C265S
The W65C265S is a powerful and flexible 16-bit microcontroller based on the W65C816S.
Product Features:
W65C816S CPU
Embedded Debug Monitor ROM
Debug port UART with baud rate timer
576 bytes of RAM
64 I/O Lines
(3) 16-bit timers with maskable interrupts
Parallel Interface Bus (PIB)
(3) UARTs with baud rate timers
Monitor "Watch Dog" Timer with "restart" interrupt
Twin Tone Generators

## Slide 6: Peripheral Interface Adapter (PIA) W65C21S
The W65C21S is a very flexible Peripheral Interface Adapter (PIA) for use with WDC’s 65xx and other 8-bit microprocessor families.
Product Features:
Two 8-bit bidirectional I/O ports with per bit data direction control.
Automatic “Handshake” control of data transfers
(4) Programmable interrupt control lines (two for each port)
Register and Chip Selects specified for multiplexed operation

## Slide 7: Versatile Interface Adapter (VIA) W65C22S
The W65C22S VIA combines flexible I/O control with the added versatility of (2) 16-bit Timers.
Product Features:
Two 8-bit bi-directional I/O ports with per bit data direction control.
Automatic “Handshake” control of data transfers
(4) Programmable interrupt control lines (two for each port)
Register and Chip Selects specified for multiplexed operation
Two 16-bit programmable Interval Timer/Counters
Synchronous serial port

## Slide 8: Asynchronous Communications Interface Adapter (ACIA) W65C51S
The W65C51S Asynchronous Communications Interface Adapter (ACIA) provides a program controlled interface between microprocessor based systems and serial communication data sets and modems.
Product Features:
Full duplex operation with buffered receiver and transmitter
Data set/modem control functions
Internal baud rate generator with 15 programmable baud rates (50 to 19,200)
Programmable word lengths, number of stop bits and parity bit generation and detection
Program-selectable serial echo mode

## Slide 9: Replacements
-W65C02S-
Replacement For:
CMD/GTE - G65SC02
MOS Technology - 6502
Rockwell – R6502, R65C02
-W65C21S-
Replacement For:
AMI – 6820, 6821
CMD/GTE - G65SC21
Hitachi – HD6821, HD6321
MOS Technology - 6521
Motorola – M6820, M6821
Rockwell – R6520, R6521, R65C21
ST Micro. – EF6821
As One of The Original Sources of 65xx Technology, WDC provides Parts Previously Offered By Our Licensees and Others.
All of Our Parts Are RoHS/Green/Pb-Free Compliant
-W65C22S-
Replacement For:
CMD/GTE - G65SC22
MOS Technology - 6522
Rockwell – R6522, R65C22, R65NC22
-W65C51S-
Replacement For:
AMI – 6551
CMD/GTE - G65SC51
Harris – CDP65C51
MOS Technology - 6551
Rockwell – R6551, R65C51
Synertek - 6551